| No. | Technical Specification | Min Requirement | Bidder Offer |
| --- | --- | --- | --- |
| 1 | Manufacturer | Please specify Manufacturer and country of origin (USA, Europ, Japan) |  |
| 2 | Model Number | Please specify model number of the offered equipment |  |
| 3 | Safety Standard | FDA or CE marking |  |
| 4 | Desine and Quality | Compact heavy duty and high quality |  |
| 5 | Ventilator System | Microprocessor controlled used for Adult, Pediatric Software must be upgradable Humidifier Compressor (optional) Nebulizer (standard) Leak compensation |  |
| 6 | Ventilator mode | Volume controlled Pressure controlled (APRV) SIMV Spontaneous pressure support/ CPAP Non invasive PRVC |  |
| 7 | Special functions | Pediatric , Adult applecation Apnea back up ventilation Standby Manual breaths Measure static and dynamic parameter High frequency ventilation mode (optional) |  |
| 8 | Graphic waveform, trends & loops Minimume 3 waveform | Flow Volume Pressure Other specify |  |
| 9 | Display | Multicolor LCD display not less than "10" Preferable touch screen With easy to use inter face |  |
| 10 | Ventilator monitoring parameters | Inspiratory peak flow Expired tidal volume Pressure (peak inspiratory,mean, peep) Inspired oxygen concentration Fio2 I:E ratio frequency |  |
| 11 | Trigger mechanism | pressure, flow |  |
| 12 | Alarm limits (adjustable) | low/high pressure limit low Fio2 low/high PEEP/CPAP pressure High /low tidal volume low minute volume low/high respiratory rate low/high Fio2 :21-100% Apnea: 5-20 sec. All alarms audible and visible |  |
| 13 | Power supply | 220v 50Hz (built in)Battery back up not less than 30min |  |
| 14 | Equipment alarm | Power failure Low Battery Disconnection Gas supply failure Flow sensore alarms All alarms audible and visible |  |
| 15 | Self diagnostic error/calibration massage | Included |  |